Quaternions

A small rotation vector can easily be converted to quaternion, think of a small step $\delta \alpha \in \mathbb{R}^{3}$on a 2D plane mapped to a 3D sphere (Figure \ref{quaternion}, Equation \ref{quat_delta}). This small translation can altered to quaternion space for optimisation purposes (used in later sections) by approximating $\delta \alpha$ as $\Delta \alpha$ (Equation \ref{quat_opt}).

\begin{equation}
\label{quat_delta}
\delta \textbf{q} = \exp{ \bigg(
    \begin{bmatrix}
        \frac{1}{2}\delta \alpha \\[0.3em]
       0
     \end{bmatrix} \bigg) }= \begin{bmatrix}
        \sin \Vert \frac{\delta \alpha}{2} \Vert \frac{\delta \alpha}{2} \\[0.3em]
       \cos \Vert \frac{\delta \alpha}{2} \Vert
     \end{bmatrix} ^{\oplus}
\end{equation}

\begin{equation}
\label{quat_opt}
\overline{q}^{k+1} = \delta \textbf{q}(\Delta \alpha) \otimes \overline{q}^{k}
\end{equation}

SLAM

The SLAM problem is therefore formulated using both re-projection error (from the camera measurements) $\textbf{e}_{r}$ and an inertial error term from the IMU $\textbf{e}_{s}$.

\begin{equation}
\begin{aligned}
J(x) := \sum_{i=1}^{I} \sum_{k=1}^{K}\sum_{j \in \mathcal{J}(i,k)} \textbf{e}_{r}^{i,j,k \textnormal{ } T} \textbf{W}_{r}^{i,j,k} \textbf{e}_{r}^{i,j,k} +
\sum_{k=1}^{K-1} \textbf{e}_{s}^{k \textnormal{ } T} \textbf{W}_{s}^{k} \textbf{e}_{s}^{k}
\end{aligned}
\end{equation}

where $i$ is the camera index, $k$ the camera frame index, $j$ the landmark index. Indices of landmarks in the $k$th frame and $i$th camera are in the set $\mathcal{J}(i,k)$. In the case of this project the error is only estimated with one camera, and the IMU. Any additional sensors used would also need to be included in this error state.